## Slide 1: BunnyHop: Exploiting The Instruction Prefetcher
Zhiyuan Zhang, Mingtian Tao, Sioli O’Connell,
Chitchanok Chuengsatiansup, Daniel Genkin, Yuval Yarom

## Slide 2: BunnyHop
CMP value, 1
JE Target
Target
NOP
NOP
NOP
NOP
Instruction Prefetcher
Cache
Branch Predictor
NOP
Target
We like shared resources !
The Bunny Hops!
NOP
NOP
NOP
NOP
NOP
NOP
Branch Here?
Response
Target
NOP
Hey prefetcher, check an address.
Target
Cache Attack.
Okey-Dokey!
BunnyHop: Translate Branch Predictor State to Cache State

## Slide 3: With the Power of BunnyHop
Reverse Engineer
  First work on Instruction Prefetcher
  Branch Target Buffer
    First work on Replacement Policy
    First observation of two type branches: Long Branch & Short Branch
Three Cool Attacks
  Flush+Reload on Predictor: Learn same thread predictor state
  Prime+Probe on Predictor: Learn cross-thread predictor state
  Self-Eviction : Confuse the victim to evict its own data
More in the paper!

## Slide 4: Self-Eviction: The Resident Evil
Evict secret-dependent data from cache
S
JMP
JMP
JMP
JMP
Cache Coloring
Poison the Branch Predictor
Poison
Guide
Prefetch
Any Instruction
Measure victim process
Evict
Evict

## Slide 5: Self-Eviction: The case of AES

## Slide 6: Summary
Branch Predictor state can be leaked via cache state
Reverse Engineer the Instruction Prefetcher
Reverse Engineer the Branch Target Buffer
Three attacks on Branch Predictor
https://github.com/0xADE1A1DE/BunnyHop
Paper
Code
Notes: Give a list of what we have done.